## Slide 1
Risk-Aware Lane-Change Planning
via Online CVaR-Augmented MPPI
Ayush Agrawal · ECE M237 (Dynamic Programming) · UCLA Spring 2026

## Slide 2
When optimising the mean isn't enough.
• Highway lane-changes: hundreds of routine outcomes for every catastrophic one.
• Standard MPC averages over all of them — the catastrophic 1-in-20 is invisible.
• The right object for that tail is CVaR.

## Slide 3
Two ideas in one slide.
MPPI = best-of-many-random-plans, weighted by cost.
Not just the mean, not just the worst case — the average over the bad tail.

## Slide 4
Online CVaR inside MPPI's cost aggregator.
min E[J_task] s.t. CVaR_α( L_risk ) ≤ C_u
 | Offline CVaR-MDP (Chow 2015) | Online CVaR-MPPI (this work)
CVaR computed | Pre-computed VI table (state × budget) | Monte-Carlo, every 50 ms
Continuous state? | Exponential blow-up | Sampling-based
Re-tunable in deploy? | Rebuild table | Change C_u & rerun
Real-time? | Offline | ≈ 80 ms / cycle on CPU

## Slide 5
Same seed. Same noise. Different aggregator. Different outcome.
MPPI — crashed @ 6.5 s
CVaR-MPPI — survived 20 s
75 × TTC margin
 | MPPI | CVaR-MPPI
Outcome | 🔴 crashed 6.5 s | 🟢 survived 20 s
TTC_min | 0.01 s | 0.75 s
e_y,RMS | 0.762 m | 0.219 m
a_y,peak | 15.2 m/s² | 17.1 m/s² (cost of safety)

## Slide 6
Across 30 paired runs — three stories.
Scenario | Seeds | MPPI crash | CVaR crash | Notable per-seed
lane_change (mixed dir.) | 10 | 0/10 | 1/10 ⚠ | seed 2: CVaR collides where MPPI survived
cutin | 10 | 1/10 | 1/10 | seed 2: min_dist 2.19 → 4.31 m (+97 %)
hard_brake (paired) | 1 | False | False (bit-identical) | CVaR silent ⇒ no-regret ✓
⭐
Helps decisively when F̃ spans the hazard (single-seed lane_change).
🟰
Silent when baseline is already safe — bit-identical trajectories on hard_brake = no-regret.
⚠
Can regress on noisy-tail seeds (sweep seed 2). Parameter-sensitive.

## Slide 7
What I learned.
🎯
CVaR helps only when F̃ spans the hazard.
Scripted out-of-distribution braking ⇒ silent; natural traffic perturbations ⇒ active.
🛡
No-regret is provable and verified.
J_C ≡ 0 ⇒ S̃ = S bit-for-bit (confirmed on hard_brake).
🔧
Calibrating C_u is the hardest knob.
Built per-step n_over_budget / cvar_max logging so the penalty's activity is observable, not assumed.
📉
Soft constraints can regress at the margin.
Future work: hard-constrained CVaR via Chow's confidence-set formulation.
Online CVaR-MPPI delivers selective tail shaping: invisible when unneeded, decisive when needed, transparent when wrong.